## Slide 1: Exploring Environmental Science for AP®
1st Edition
Chapter 19
Air Pollution and Ozone Depletion
Copyright © 2018 Cengage Learning. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Core Case Study: Los Angeles Air Pollution
1950s: Los Angeles air was among dirtiest in the world
  Industrial emissions
  Motor vehicle emissions
Public protest over smog in the 1950s and 1960s
1970: Congress passed the Clean Air Act
  Mandated pollution control measures
    Resulted in dramatic improvements in air quality

## Slide 3: 19.1 What Is the Nature of the Atmosphere?
Innermost layers of the atmosphere
  Troposphere
    Supports life
  Stratosphere
    Contains the protective ozone layer

## Slide 4: The Atmosphere Consists of Several Layers (1 of 2)
Atmosphere
  Thin blanket of gases surrounding the earth
Density
  Number of gas molecules per unit of air volume
  Decreases with higher altitude
Atmospheric pressure
  Force per unit area of a column of air
  Decreases with higher altitude

## Slide 5: The Atmosphere Consists of Several Layers (2 of 2)
Notes: Figure 18.2 Natural capital. The earth’s atmosphere is a dynamic system that includes four layers. The average temperature of the atmosphere varies with altitude (red line) and with differences in the absorption of incoming solar energy. Critical thinking: Why do you think most of the planet’s air is in the troposphere?

## Slide 6: Air Movement and Chemicals in the Troposphere Affect the Earth’s Weather and Climate
Troposphere
  75–80% of the earth’s air mass
  Closest to the earth's surface
  Composition of gases
    78% nitrogen and 21% oxygen
Rising and falling air currents and greenhouse gases play major roles in weather and climate
  Greenhouse gases include H2O, CO2, CH4, and N2O

## Slide 7: The Stratosphere Is Our Global Sunscreen
Stratosphere: 17–48 kilometers above the earth’s surface
  Similar composition to troposphere except:
    Lower volume of water vapor
    Higher concentration of ozone (O3)
Ozone layer
  Filters 95% of harmful UV radiation
  Allows life to exist on land

## Slide 8: 19.2 What Are the Major Outdoor Air Pollution Problems?
Industrial smog
  Caused primarily by burning coal
Photochemical smog
  Caused by emissions from motor vehicles, industrial facilities, and power plants

## Slide 9: Air Pollution Comes from Natural and Human Sources (1 of 4)
Air pollution–presence of chemicals in the atmosphere
  Concentrations high enough to harm organisms, ecosystems, human-made materials, or alter climate
Natural sources
  Wind-blown dust
  Pollutants from wildfires or volcanic eruptions
  Volatile organics released by plants

## Slide 10: Air Pollution Comes from Natural and Human Sources (2 of 4)
Human sources
  Mostly in industrialized and urban areas
  Stationary sources
    Power plants and industrial facilities
  Mobile sources
    Motor vehicles

## Slide 11: Air Pollution Comes from Natural and Human Sources (3 of 4)
Primary pollutants
  Emitted directly into the air
Secondary pollutants
  Formed from reactions of primary pollutants

## Slide 12: Air Pollution Comes from Natural and Human Sources (4 of 4)
Notes: Figure 18.3 Human inputs of air pollutants come from mobile sources (such as cars) and stationary sources (such as industrial, power, and cement plants). Some primary air pollutants react with one another and with other chemicals in the air to form secondary air pollutants.

## Slide 13: Air Pollution Has Harmful Effects
Air pollutants flow north to form arctic haze
Since the 1970s, outdoor air quality has improved in more-developed countries
Fine particles can get lodged in the lungs
  Contributes to cancer, asthma, heart attack, and stroke
Study: outdoor air pollution kills 1.4 million people per year in China
  645,000 per year in India

## Slide 14: Major Outdoor Air Pollutants (1 of 4)
Carbon oxides
  Carbon monoxide (CO) and carbon dioxide (CO2)
Nitrogen oxides and nitric acid
  Acid deposition
  Role in photochemical smog
Sulfur dioxide and sulfuric acid
  Reduce visibility and aggravate breathing problems

## Slide 15: Major Outdoor Air Pollutants (2 of 4)
Particulates
  Suspended particulate matter
Ozone
  Can cause coughing and breathing problems
Volatile organic compounds (VOCs)
  Methane
  Benzene, dry-cleaning fluids, and various components of gasoline and plastics

## Slide 16: Major Outdoor Air Pollutants (3 of 4)
TABLE 18 1 Chemical Reactions that Form Major Air Pollutants
Notes: Table 18.1 Chemical reactions that form major air pollutants

## Slide 17: Major Outdoor Air Pollutants (4 of 4)
Notes: Figure 18.4 Sulfuric acid and other air pollutants have damaged this statue in Rome, Italy. The nose and part of the forehead have been restored.

## Slide 18: Case Study: Lead Is a Highly Toxic Pollutant (1 of 2)
In air, water, soil, plants, and animals
Does not break down in the environment
Impacts human health and environment
  Children most vulnerable
  Can cause death, brain damage, and paralysis
Lead exposure for adults and children working in e-waste recycling

## Slide 19: Case Study: Lead Is a Highly Toxic Pollutant (2 of 2)
Insert figure 19.6

## Slide 20: Burning Coal Produce Industrial Smog (1 of 3)
Chemical composition of industrial smog
  Sulfur dioxide, sulfuric acid, and suspended solid particles
Combustion of coal and oil forms carbon monoxide, carbon dioxide, and soot
Common in industrialized urban areas
  Examples: China, India, Ukraine
  Beijing air quality among world’s worst

## Slide 21: Burning Coal Produces Industrial Smog (2 of 3)
Notes: Figure 18.7 A greatly simplified model of how pollutants are formed when coal and oil are burned. The result is industrial smog.

## Slide 22: Sunlight Plus Cars Equals Photochemical Smog
Photochemical smog formed under the influence of sun’s UV radiation
VOCs + NOx + heat + sunlight yields:
  Ground level O3 and other photochemical oxidants
  Aldehydes
  Other secondary pollutants

## Slide 23: Burning Coal Produces Industrial Smog (3 of 3)
Notes: Figure 18.8 A greatly simplified model of how the pollutants that make up photochemical smog are formed.

## Slide 24: Critical Concept: Factors Affecting Outdoor Air Pollution (1 of 3)
Factors that help reduce outdoor air pollution
  Gravity allows particulates to settle
  Rain and snow
  Salty sea spray from the ocean
  Winds
  Natural chemical reactions remove some pollutants

## Slide 25: Several Factors Affect Levels of Outdoor Air Pollution (2 of 3)
Factors that increase outdoor air pollution
  Urban buildings
  Hills and mountains
  High temperatures
  VOC emissions from certain trees and plants
  The grasshopper effect
  Temperature inversion
    Warm air above cool air prevents mixing

## Slide 26: Several Factors Affect Levels of Outdoor Air Pollution (3 of 3)
Notes: Figure 18.9 A temperature inversion can take place in either of the two sets of topography and weather conditions shown here. Polluted air can be trapped between mountain ranges and under the inversion layer (left). Or it can be blown by sea breezes and trapped against a mountain range and under the conversion layer (right, see Core Case Study).

## Slide 27: 19.3 What Is Acid Deposition and Why Is It a Problem?
Caused mainly by coal-burning power plants and motor vehicle emissions
Threatens human health, aquatic life and ecosystems, forests, and human-built structures

## Slide 28: Acid Deposition (1 of 3)
Human-generated NOx and SOx in the atmosphere
Wet deposition
  Acidic rain, snow, fog, or cloud vapor
Dry deposition
  Acidic particles
Substances remain in the atmosphere for 2–14 days

## Slide 29: Acid Deposition (2 of 3)
Notes: Figure 18.11 Natural capital degradation: Acid deposition, which consists of rain, snow, dust, or gas with a pH lower than 5.6, is commonly called acid rain. Critical thinking: What are three ways in which your daily activities contribute to acid deposition?

## Slide 30: Acid Deposition (3 of 3)
Notes: Figure 18.12 This map shows regions where acid deposition is now a problem and regions with the potential to develop this problem. Such regions have large inputs of air pollution (mostly from power plants, industrial facilities, and ore smelters) or are sensitive areas with naturally acidic soils and bedrock that cannot neutralize (buffer) additional inputs of acidic compounds. Critical thinking: Do you live in or near an area that is affected by acid deposition or an area that is likely to be affected by acid deposition in the future?

## Slide 31: Harmful Effects of Acid Deposition
Contributes to respiratory disorders
Releases toxic metals from soils and rocks
  Bioaccumulation in fish
Lowers pH in aquatic ecosystems
Leaches soil nutrients
Damages forests
Damages statues and buildings

## Slide 32: Reducing Acid Deposition (1 of 2)
Prevention is always less costly than cleanup
Using renewable energy sources reduces the impact of acid rain

## Slide 33: Harmful Effects of Acid Deposition (2 of 2)
Notes: Figure 18.14 Ways to reduce acid deposition and its damage. Critical thinking: Which two of these solutions do you think are the best ones? Why?

## Slide 34: 19.4 What Are the Major Indoor Air Pollution Problems?
Indoor air pollutants
  Smoke and soot from burning wood and coal in cooking fires
    Mostly in less-developed countries
  Cigarette smoke
  Chemicals used in building materials and cleaning products

## Slide 35: Indoor Air Pollution Is a Serious Problem (1 of 3)
Less-developed countries
  Indoor burning of wood, charcoal, dung, crop residues, and coal
  Greatest risk to low-income populations
More-developed countries
  Tobacco smoke
  Formaldehyde
  Radioactive radon-222 gas
  Very small particles

## Slide 36: Indoor Air Pollution Is a Serious Problem (2 of 3)
Notes: Figure 18.16 Numerous indoor air pollutants are found in most modern homes (concept 18.4). Question: To which of these pollutants are you exposed?

## Slide 37: Indoor Air Pollution Is a Serious Problem (3 of 3)
Levels of some common air pollutants
  Two to five times higher inside U.S. homes and buildings than outdoors
  Sometimes up to 100 times higher
Pollution levels inside cars
  Up to 18 times higher than outside levels
Most people in more-developed urban areas spend 70% or more of their time indoors or inside vehicles

## Slide 38: Case Study: Radioactive Radon Gas (1 of 2)
Sources
  Underground deposits of certain minerals
Human health risks
  Decays into polonium-210
    Can expose lung tissue to large amounts of radiation
EPA recommendation
  Conduct radon tests

## Slide 39: Case Study: Radioactive Radon Gas (2 of 2)
Notes: Figure 18.18 Ways that radon-222 gas can enter homes and other buildings. Question: Has anyone tested the indoor air where you live for radon-222?

## Slide 40: 19.5 What Are the Health Effects of Air Pollution?
Air pollution can contribute to:
  Asthma
  Chronic bronchitis
  Emphysema
  Lung cancer
  Heart attack
  Stroke

## Slide 41: Your Body’s Natural Air Pollution Defenses Can Be Overwhelmed (1 of 4)
Respiratory system protection mechanisms
  Hair
  Cilia
  Mucus
Effects of smoking and prolonged air pollution exposure
  Chronic bronchitis
  Emphysema

## Slide 42: Your Body’s Natural Air Pollution Defenses Can Be Overwhelmed (2 of 4)
Notes: Figure 18.19 Major components of the human respiratory system can help to protect us from air pollution, but these defenses can be overwhelmed or breached.

## Slide 43: Your Body’s Natural Air Pollution Defenses Can Be Overwhelmed (3 of 4)
125,000 people develop cancer in the United States each year from breathing diesel fumes
14% of the U.S. population exposed to excessive particulate pollution levels daily

## Slide 44: Your Body’s Natural Air Pollution Defenses Can Be Overwhelmed (4 of 4)
Notes: Figure 18.20 Distribution of premature deaths from air pollution in the United States, mostly from very small, fine, and ultrafine particles added to the atmosphere by coal-burning power plants. Critical thinking: Why do the highest death rates occur in the eastern half of the United States? If you live in the United States, what is the risk at your home or where you go to school?

## Slide 45: 19.6 How Should We Deal with Air Pollution?
Legal, economic, and technological tools can help clean up air pollution
  Best solution is to prevent it

## Slide 46: Laws and Regulations Can Reduce Outdoor Air Pollution (1 of 3)
United States
  Clean Air Acts: 1970, 1977, and 1990 created regulations enforced by states and cities
EPA
  Established air quality standards for six outdoor pollutants
    Carbon monoxide, nitrogen dioxide, sulfur dioxide, suspended particulate matter, ozone, and lead

## Slide 47: Laws and Regulations Can Reduce Outdoor Air Pollution (2 of 3)
EPA’s national emission standards for 188 hazardous air pollutants (HAPs)
  Toxic Release Inventory (TRI)
New U.S. regulations
  Limit CO2 emissions from coal-fired power plants
New air quality standards in China
  Ban on high-sulfur, high-ash-content coal in major cities

## Slide 48: Laws and Regulations Can Reduce Outdoor Air Pollution (3 of 3)
Insert figure 19.19

## Slide 49: Using the Marketplace to Reduce Outdoor Air Pollution
Buy and sell air pollution allotments in the marketplace
  1990 Clean Air Act authorized emissions trading or cap-and-trade program
  Success depends on:
    How low initial cap is set
    How often it is lowered

## Slide 50: Other Ways to Reduce Outdoor Air Pollution (1 of 4)
Technologies used on coal-burning power plants
  Electrostatic precipitator
  Wet scrubber
Motor vehicle pollution
  Prevention and reduction

## Slide 51: Ways to Reduce Outdoor Air Pollution (2 of 4)
Notes: Figure 18.24 An electrostatic precipitator (left) and a wet scrubber (right) are used to reduce particulate and SO2 emissions from coal-burning power and industrial plants.

## Slide 52: Ways to Reduce Outdoor Air Pollution (3 of 4)
Notes: Figure 18.23 Ways to prevent, reduce, or disperse emissions of sulfur oxides, nitrogen oxides, and particulate matter from stationary sources, especially coal-burning power plants and industrial facilities (Concept 18.6). Critical thinking: Which two of these solutions do you think are the best ones? Why?

## Slide 53: Case Study: Revisiting Air Pollution in Los Angeles
Lowest pollution levels since 1999
Largest sources of pollutants
  Ports of Los Angeles and Long Beach
    Most ships burn diesel fuel
Pollution is trapped by mountain ranges; builds up during thermal inversions

## Slide 54: Ways to Reduce Outdoor Air Pollution (4 of 4)
Notes: Figure 18.25 Ways to prevent or reduce emissions from motor vehicles (Concept 18.6). Critical thinking: Which two of these solutions do you think are the best ones? Why?

## Slide 55: Reducing Indoor Air Pollution (1 of 3)
Greater threat to human health than outdoor pollution
What can be done?
  Prevention
  Cleanup

## Slide 56: Reducing Indoor Air Pollution (2 of 3)
Notes: Figure 18.27 Ways to prevent or reduce indoor air pollution (Concept 18.6). Critical thinking: Which two of these solutions do you think are the best ones? Why?

## Slide 57: Reducing Indoor Air Pollution (3 of 3)
Insert figure 19.25
Notes: Figure 18.28 Individuals matter: You can reduce your exposure to indoor air pollution. Critical thinking: Which three of these actions do you think are the most important ones to take? Why?

## Slide 58: 19.7 How Have We Depleted Ozone in the Stratosphere and What Can We Do About It?
Widespread use of certain chemicals
  Reduced ozone levels in the stratosphere
  Allowed more harmful ultraviolet radiation to reach the earth’s surface
Actions necessary to reverse ozone depletion
  Stop producing ozone-depleting chemicals
  Adhere to international treaties banning such chemicals

## Slide 59: The Use of Certain Chemicals Threatens the Ozone Layer (1 of 2)
Ozone is thinning over Antarctica and the Arctic
Chlorofluorocarbons (CFCs)
  Persistent chemicals that attack ozone in the stratosphere
  Tales 11 to 20 years to reach the stratosphere from ground level
  CFC molecule attacks O3 and strips off a free oxygen
  Combines with Cl- to form ClO
  Each chlorine atom can break down hundreds of O3 molecules

## Slide 60: The Use of Certain Chemicals Threatens the Ozone Layer (2 of 2)
Notes: Figure 18.29 Natural capital degradation: The colorized satellite image shows ozone thinning over Antarctica during October of 2015 at its annual peak extent. Ozone depletion of 50% or more occurred in the center blue area.

## Slide 61: Why Should We Worry About Ozone Depletion?
Ozone protects the earth’s surface from damaging UV radiation
  Human health concerns
  UV radiation affects plankton, crucial for removing CO2 from the atmosphere

## Slide 62: Reversing Stratospheric Ozone Depletion
Stop producing ozone-depleting chemicals immediately
  Will take at least 60 years to recover to 1980 levels
Agreements with a prevention approach
  Montreal Protocol
    Cut emissions of CFCs
  Copenhagen Amendment
    Accelerated phase-out of CFCs

## Slide 63: Effects of Ozone Depletion
Insert figure 19.27